Query table of ultrasonic level difference meter

Note: For the first time to enter the menu, please long press SET key for two seconds.

# Text boxes

Level 1 menu

Probe1

Probe2

Level 2 menu

0 End setting

1 Parameter lock

2 Range setting

3 Measurement mode

0 End setting

1 Unlock

2 Global lock

Level 3 menu

0 End setting

1 Reference point1

2 Low range1

3 High range1

Set password

4 Reference point2

5 Low range2

6 High range2

7 Display unit

0 End setting

1 Mode selection

2 Response speed

3 Security level

Level measurement

Distance measurement

Slow

Medium speed

Fast

Keep

Minimum

Maximum

Setting value

Set current

4 Probe setting

5 Algorithm selection

6 Alarm setting

7 Parameter correction

0 end setting

1 probe mode1

2 blind area setting1

3 probe mode2

Blind area setting2

1

2

3

4

5

6

7

8

9

1

2

3

4

5

6

7

8

9

Special environment1

Special environment2

Special environment3

Special environment4

Special environment5

Special environment6

Special environment7

0 End setting

1 Alarm1 mode

2 Alarm1 value

3 Alarm1 return difference

Close

Low level alarm

High level alarm

4 Alarm2 mode

5 Alarm2 value

6 Alarm2 return difference

7 Alarm3 mode

Close

Low level alarm

High level alarm

Close

Low level alarm

High level alarm

8 Alarm3 value

9 Alarm3 return difference

10 Alarm4 mode

11 Alarm4 value

Close

Low level alarm

High level alarm

12 Alarm4 return difference

0 End setting

1 Range correction

2 Sound speed correction

3 4mA correction1

4 20mA correction1

5 Reference current1

6 4mA correction2

7 20mA correction2

8 Reference current2

8 Communication setting

9 Work mode

10 Reset options

0 End setting

1 Communication address

3 Baud rate

2400

4800

9600

19200

Double level

Absolute difference

Relative difference

Average value

0 End setting

1 Mode selection

2 mAOUT2

3 4mA corresponding difference

4 20mA corresponding difference

0 End setting

1 Factory reset

2 System reset

m

cm

mm

Yes

No

Yes

No